## Slide 1
OFFICIAL · WINN FAMILY ASSOCIATION · TRAINING CENTRE
DOCUMENT REFERENCE
WFA/TC/WFA1208
Issue 1 · 2 November 2026
Classification: OFFICIAL
TRAINING CENTRE MODULE · WFA1208
DRAINAGE AND WET WEATHER MANAGEMENT
Ground & Pitch Preparation • Intermediate • About 35 minutes • 7 lessons • 12-question test
Learn how water leaves a cricket ground, how aeration and drains help, and how to get play back on safely after rain.
WINN FAMILY T-20 LEAGUE · OPERATING UNDER THE AUTHORITY OF THE WINN FAMILY ASSOCIATION
Notes: TITLE — say: Welcome to WFA1208 Drainage and Wet Weather Management, an official Winn Family Association Training Centre module. Learn how water leaves a cricket ground, how aeration and drains help, and how to get play back on safely after rain.

## Slide 2
DOCUMENT CONTROL
AUTHORISATION & MODULE DETAILS
MODULE | WFA1208 Drainage and Wet Weather Management
REFERENCE | WFA/TC/WFA1208 · Issue 1
DISCIPLINE | Ground & Pitch Preparation · Intermediate · About 35 minutes
ASSESSMENT | 12 questions · 80% to pass
REQUIRED FIRST | WFA1206 Soil, Moisture and Surface Conditions
ISSUING BODY | Winn Family Association — Training Centre
AUTHORISED BY | Alex Winn, League Founder & Director
AWARD | WFA certificate of completion on a pass (a WFA award, not an external qualification)
Notes: DOCUMENT CONTROL — this deck is an official Winn Family Association document. Reference WFA/TC/WFA1208. Authorised by Alex Winn, League Founder & Director.

## Slide 3
MODULE OVERVIEW
ABOUT THIS MODULE
WFA1208 – Drainage and Wet Weather Management explains how a cricket ground copes with rain. You will learn about surface and sub-surface drainage, compaction and aeration, how to identify problem areas, the tools used to remove surface water, and how the ground team supports umpires in getting play restarted safely after rain. This is a WFA award, not an ECB qualification: for recognised groundsmanship training see the ECB's groundsmanship resources and courses (including its TS4 pitch and outfield guidance), and the ICC's pitch-curation guidance.
The module is for members who have completed WFA1206 and want to help when the weather turns. Aeration machinery and water removal equipment must only be used by trained and authorised people, and any major drainage work needs professional advice. This module is not a substitute for accredited training. Completing it earns the WFA Wet Weather Response recognition.
WHAT YOU'LL GET
Your WFA1208 Drainage and Wet Weather Management Badge
Awarded upon successfully completing the WFA1208 Drainage and Wet Weather Management training module, recognising your knowledge of drainage, aeration and safe wet weather response at Winnston Park.
Your Certificate of Completion
Official certification confirming you have successfully completed the WFA1208 Drainage and Wet Weather Management course and met all required training standards.
WFA Wet Weather Response Recognition
Recognises your knowledge of drainage and wet weather management, helping the ground team get cricket back on safely after rain.
Notes: OVERVIEW — say: WFA1208 – Drainage and Wet Weather Management explains how a cricket ground copes with rain. You will learn about surface and sub-surface drainage, compaction and aeration, how to identify problem areas, the tools used to remove surface water, and how the ground team supports umpires in getting play restarted safely after rain. This is a WFA award, not an ECB qualification: for recognised groundsmanship training see the ECB's groundsmanship resources and courses (including its TS4 pitch and outfield guidance), and the ICC's pitch-curation guidance. The module is for members who have completed WFA1206 and want to help when the weather turns. Aeration machinery and water removal equipment must only be used by trained and authorised people, and any major drainage work needs professional advice. This module is not a substitute for accredited training. Completing it earns the WFA Wet Weather Response recognition.

## Slide 4
WE ARE HERE TO HELP
NEED HELP? JUST ASK
DURING THE SESSION
Put your hand up or ask your coach — there is no such thing as a silly question.
Finding it hard, or too easy? Ask — every activity can be made easier or harder.
Hurt, unwell or feeling dizzy? Stop, sit out and tell a coach straight away.
Need water, a break or the toilet? Just let a coach know.
WORRIED ABOUT SOMETHING?
If anything or anyone makes you feel unsafe or upset, tell your coach or the Welfare Officer — the same day.
You can also report a concern online at winnfamilyleague.com/association/safeguarding.
In an emergency, call 999.
AFTER THE SESSION
Questions about today? Email info@winnfamilyleague.com.
Your certificates, progress and feedback form are in the members' area — winnfamilyleague.com/my.
Free one-to-one coaching for league members, any day 9am–6pm.
Notes: NEED HELP? — read this slide out and point to where the coaches and the Welfare Officer are. Say: "If you get stuck, feel unwell or something is worrying you, tell one of us straight away. Nobody will ever be in trouble for asking for help." Check for anyone who needs an adaptation (injury, medical condition, access needs) and agree it quietly now. Stuck on a lesson or the test? Members can ask through the module page, or email the Training Centre team.

## Slide 5
YOUR LEARNING PATHWAY
WHERE THIS MODULE FITS
REQUIRED FIRST
WFA1206 Soil, Moisture and Surface Conditions
RECOMMENDED PREPARATION
No extra preparation needed.
THIS MODULE UNLOCKS
The next stage of your pathway.
Notes: REQUIRED — the test unlocks only once these are passed: WFA1206 Soil, Moisture and Surface Conditions.

## Slide 6
07
THE LESSONS
1. How Water Leaves a Ground · 2. Compaction and Why It Matters · 3. Aeration · 4. Identifying Problem Areas · 5. Removing Surface Water · 6. Getting Play Back On · 7. Safety in Wet Weather
Notes: This module has 7 lessons.

## Slide 7
LESSON 1 OF 7
HOW WATER LEAVES A GROUND
KEY POINTS
Surface run-off along gentle falls
Infiltration through the root zone
Pipes, slit drains and sand bands
Evaporation and the grass itself
IN THIS LESSON
In this lesson you will learn the routes water takes on a cricket ground. Some runs off the surface, guided by gentle falls in the levels towards the boundary. Some soaks into the soil and moves down through the root zone. Where the natural soil drains poorly, installed drainage such as pipes, slit drains or sand bands carries the water away to an outlet. Some returns to the air through evaporation and the grass itself. A good ground uses all of these. When one fails, for example when the surface is compacted or a drain outlet is blocked, water sits on the surface and play is lost.
Notes: LESSON 1 — HOW WATER LEAVES A GROUND — say: In this lesson you will learn the routes water takes on a cricket ground. Some runs off the surface, guided by gentle falls in the levels towards the boundary. Some soaks into the soil and moves down through the root zone. Where the natural soil drains poorly, installed drainage such as pipes, slit drains or sand bands carries the water away to an outlet. Some returns to the air through evaporation and the grass itself. A good ground uses all of these. When one fails, for example when the surface is compacted or a drain outlet is blocked, water sits on the surface and play is lost. Key points: Surface run-off along gentle falls; Infiltration through the root zone; Pipes, slit drains and sand bands; Evaporation and the grass itself.

## Slide 8
LESSON 2 OF 7
COMPACTION AND WHY IT MATTERS
KEY POINTS
Traffic squeezes out air spaces
Water then sits on the surface
Wanted on the square, a problem on the outfield
Look near gates and walkways
IN THIS LESSON
In this lesson you will learn about compaction, the most common cause of a wet outfield. Feet, vehicles and machinery, especially in wet conditions, press soil particles together and squeeze out the air spaces that water needs to pass through. The result is a surface that stays wet, grass with shallow roots, and moss or weeds. On the square some compaction is wanted, but on the outfield it is the enemy. Keeping vehicles off wet ground, varying routes, and relieving compaction through aeration are the key responses. Compacted areas are often near gates, sightscreens and the walkway to the square.
Notes: LESSON 2 — COMPACTION AND WHY IT MATTERS — say: In this lesson you will learn about compaction, the most common cause of a wet outfield. Feet, vehicles and machinery, especially in wet conditions, press soil particles together and squeeze out the air spaces that water needs to pass through. The result is a surface that stays wet, grass with shallow roots, and moss or weeds. On the square some compaction is wanted, but on the outfield it is the enemy. Keeping vehicles off wet ground, varying routes, and relieving compaction through aeration are the key responses. Compacted areas are often near gates, sightscreens and the walkway to the square. Key points: Traffic squeezes out air spaces; Water then sits on the surface; Wanted on the square, a problem on the outfield; Look near gates and walkways.

## Slide 9
LESSON 3 OF 7
AERATION
KEY POINTS
Holes let air and water move
Solid, slit, hollow and deep tines
Square aeration mostly outside the season
Machinery only by trained operators
IN THIS LESSON
In this lesson you will learn how aeration helps drainage. Aeration means making holes or fissures in the soil so air and water can move. Solid tines and slits are used regularly on outfields to keep channels open, while hollow tines remove cores and can help with thatch. Deep tine machines relieve compaction lower down. On the square, aeration is mainly done outside the playing season, as part of renovation, so that the pitches are not weakened. Aeration is done when the soil is moist enough for the tines to penetrate but not so wet that the machine causes damage. All aeration machinery requires training and authorisation.
Notes: LESSON 3 — AERATION — say: In this lesson you will learn how aeration helps drainage. Aeration means making holes or fissures in the soil so air and water can move. Solid tines and slits are used regularly on outfields to keep channels open, while hollow tines remove cores and can help with thatch. Deep tine machines relieve compaction lower down. On the square, aeration is mainly done outside the playing season, as part of renovation, so that the pitches are not weakened. Aeration is done when the soil is moist enough for the tines to penetrate but not so wet that the machine causes damage. All aeration machinery requires training and authorisation. Key points: Holes let air and water move; Solid, slit, hollow and deep tines; Square aeration mostly outside the season; Machinery only by trained operators.

## Slide 10
LESSON 4 OF 7
IDENTIFYING PROBLEM AREAS
KEY POINTS
Note where water stands and for how long
Moss, rushes and soft patches are warnings
Keep outlets and ditches clear
Map problem areas for the committee
IN THIS LESSON
In this lesson you will learn how to spot drainage problems. After heavy rain, walk the ground and note where water stands, how long it takes to clear, and whether the same areas are always worst. Look for moss, soft patches, rushes or black layers in the soil, which all suggest poor drainage. Check that drain outlets and ditches are clear and that gullies are not blocked with leaves. Mark the problem areas on a simple plan of the ground. This information helps the committee decide where aeration is needed or whether professional advice on drainage is worthwhile.
Notes: LESSON 4 — IDENTIFYING PROBLEM AREAS — say: In this lesson you will learn how to spot drainage problems. After heavy rain, walk the ground and note where water stands, how long it takes to clear, and whether the same areas are always worst. Look for moss, soft patches, rushes or black layers in the soil, which all suggest poor drainage. Check that drain outlets and ditches are clear and that gullies are not blocked with leaves. Mark the problem areas on a simple plan of the ground. This information helps the committee decide where aeration is needed or whether professional advice on drainage is worthwhile. Key points: Note where water stands and for how long; Moss, rushes and soft patches are warnings; Keep outlets and ditches clear; Map problem areas for the committee.

## Slide 11
LESSON 5 OF 7
REMOVING SURFACE WATER
KEY POINTS
Squeegees and brushes move water away
Water removers soak up standing water
Drying materials on footholds as umpires direct
Never let cover water run onto the square
IN THIS LESSON
In this lesson you will learn the tools used to remove surface water. Squeegees and brushes push water off the covers and away from the square. Sponge or roller water removers, sometimes known by trade names, soak up standing water and release it away from the playing area. Sawdust or drying materials may be used on bowlers' run-ups and footholds to improve grip, under the umpires' direction. Never brush water from the covers onto the square, and lift covers carefully so water runs off the edge away from the pitch. Work methodically, starting with the areas that matter most for play to resume.
Notes: LESSON 5 — REMOVING SURFACE WATER — say: In this lesson you will learn the tools used to remove surface water. Squeegees and brushes push water off the covers and away from the square. Sponge or roller water removers, sometimes known by trade names, soak up standing water and release it away from the playing area. Sawdust or drying materials may be used on bowlers' run-ups and footholds to improve grip, under the umpires' direction. Never brush water from the covers onto the square, and lift covers carefully so water runs off the edge away from the pitch. Work methodically, starting with the areas that matter most for play to resume. Key points: Squeegees and brushes move water away; Water removers soak up standing water; Drying materials on footholds as umpires direct; Never let cover water run onto the square.

## Slide 12
LESSON 6 OF 7
GETTING PLAY BACK ON
KEY POINTS
Umpires decide fitness for play
Remove covers and water efficiently
Keep umpires informed honestly
Check WFA regulations for reduced overs
IN THIS LESSON
In this lesson you will learn how the ground team supports a restart after rain. Under the Laws, the umpires decide whether conditions are fit for play, considering safety of the players above all. The ground team's job is to give them the best chance by removing covers efficiently, clearing water and making run-ups and footholds safe. Keep the umpires informed of progress and be honest about problem areas. In a Twenty20 match, overs may be reduced under the competition's rules, so time matters, but rushing that leads to a dangerous surface helps nobody. Check the WFA competition regulations for reduced-overs rules.
Notes: LESSON 6 — GETTING PLAY BACK ON — say: In this lesson you will learn how the ground team supports a restart after rain. Under the Laws, the umpires decide whether conditions are fit for play, considering safety of the players above all. The ground team's job is to give them the best chance by removing covers efficiently, clearing water and making run-ups and footholds safe. Keep the umpires informed of progress and be honest about problem areas. In a Twenty20 match, overs may be reduced under the competition's rules, so time matters, but rushing that leads to a dangerous surface helps nobody. Check the WFA competition regulations for reduced-overs rules. Key points: Umpires decide fitness for play; Remove covers and water efficiently; Keep umpires informed honestly; Check WFA regulations for reduced overs.

## Slide 13
LESSON 7 OF 7
SAFETY IN WET WEATHER
KEY POINTS
Wet surfaces are slippery, wear good grip
Move water-laden covers as a team
Stop work in thunder and lightning
Machinery can slide on wet ground
IN THIS LESSON
In this lesson you will learn to stay safe while working in the wet. Wet grass and covers are slippery, so wear footwear with good grip and move carefully. Covers full of water are very heavy, so move them as a team and never alone. Never use electrical equipment in standing water, and stop all outdoor work if there is thunder or lightning, sheltering in a building rather than under trees. Machinery can slide on wet slopes, and should only be used when the operator judges it safe. Look after yourself, as cold, wet volunteers make mistakes.
Notes: LESSON 7 — SAFETY IN WET WEATHER — say: In this lesson you will learn to stay safe while working in the wet. Wet grass and covers are slippery, so wear footwear with good grip and move carefully. Covers full of water are very heavy, so move them as a team and never alone. Never use electrical equipment in standing water, and stop all outdoor work if there is thunder or lightning, sheltering in a building rather than under trees. Machinery can slide on wet slopes, and should only be used when the operator judges it safe. Look after yourself, as cold, wet volunteers make mistakes. Key points: Wet surfaces are slippery, wear good grip; Move water-laden covers as a team; Stop work in thunder and lightning; Machinery can slide on wet ground.

## Slide 14
FURTHER LEARNING
REFERENCE VIDEOS
Sports Field Drainage System Explained | TekBerry’s Modern Water Management Design
TekBerry — Explains how piped and slit drainage move water off a sports field. · https://www.youtube.com/watch?v=BJJDkTYPuEw
The Redexim Verti-Drain®: The Original Deep Tine Aerator
Redexim — Shows deep tine aeration relieving compaction so water can drain. · https://www.youtube.com/watch?v=7l5isZC5VdA
Bowdry Water Remover
durantsports — A surface water removal machine of the kind used on squares after rain. · https://www.youtube.com/watch?v=GxnAXFZIcOc
Notes: These videos are on the module page in the members’ area. They support the lessons; watch any that help.

## Slide 15
ASSESSMENT
READY FOR THE TEST?
HOW IT WORKS
12 questions, marked instantly
80% needed to pass
Retake as often as you need
No time limit
Certificate issued automatically on a pass
Locked until you have passed: WFA1206 Soil, Moisture and Surface Conditions
Notes: ASSESSMENT — take the test from the module page in the members’ area. 12 questions, marked instantly 80% needed to pass Retake as often as you need No time limit Certificate issued automatically on a pass Locked until you have passed: WFA1206 Soil, Moisture and Surface Conditions

## Slide 16
THANK YOU
You have reached the end of WFA1208 Drainage and Wet Weather Management.
Alex Winn
League Founder & Director · Winn Family Association
Keep learning in the WFA Training Centre
Notes: CLOSE — thank the group and point them to the test and their next module.