## Slide 1
OFFICIAL · WINN FAMILY ASSOCIATION · TRAINING CENTRE
DOCUMENT REFERENCE
WFA/TC/WFA1212
Issue 1 · 2 November 2026
Classification: OFFICIAL
TRAINING CENTRE MODULE · WFA1212
SAFE USE OF GROUND EQUIPMENT
Ground & Pitch Preparation • Intermediate • About 40 minutes • 8 lessons • 12-question test
Understand risk assessment, authorisation, PPE, safe operation, fuel and chemical safety, and what to do when something goes wrong.
WINN FAMILY T-20 LEAGUE · OPERATING UNDER THE AUTHORITY OF THE WINN FAMILY ASSOCIATION
Notes: TITLE — say: Welcome to WFA1212 Safe Use of Ground Equipment, an official Winn Family Association Training Centre module. Understand risk assessment, authorisation, PPE, safe operation, fuel and chemical safety, and what to do when something goes wrong.

## Slide 2
DOCUMENT CONTROL
AUTHORISATION & MODULE DETAILS
MODULE | WFA1212 Safe Use of Ground Equipment
REFERENCE | WFA/TC/WFA1212 · Issue 1
DISCIPLINE | Ground & Pitch Preparation · Intermediate · About 40 minutes
ASSESSMENT | 12 questions · 80% to pass
REQUIRED FIRST | WFA1201 Introduction to Cricket Groundsmanship
ISSUING BODY | Winn Family Association — Training Centre
AUTHORISED BY | Alex Winn, League Founder & Director
AWARD | WFA certificate of completion on a pass (a WFA award, not an external qualification)
Notes: DOCUMENT CONTROL — this deck is an official Winn Family Association document. Reference WFA/TC/WFA1212. Authorised by Alex Winn, League Founder & Director.

## Slide 3
MODULE OVERVIEW
ABOUT THIS MODULE
WFA1212 – Safe Use of Ground Equipment sets out how the WFA expects ground equipment to be used safely. You will learn about risk assessment, training and authorisation, personal protective equipment, safe operation of mowers, rollers and powered tools, fuel and chemical safety, keeping others safe, and reporting faults and incidents. This is a WFA award, not an ECB qualification: for recognised groundsmanship training see the ECB's groundsmanship resources and courses (including its TS4 pitch and outfield guidance), and the ICC's pitch-curation guidance.
The module is for every member who will work on the ground, and should be completed early in the pathway. It gives awareness of safe practice but is not a substitute for accredited machinery or chemical training, the manufacturer's instructions, or professional health and safety advice. Under-18s must not operate powered machinery and should only help with supervised, low-risk tasks. Completing it earns the WFA Ground Safety Awareness recognition.
WHAT YOU'LL GET
Your WFA1212 Safe Use of Ground Equipment Badge
Awarded upon successfully completing the WFA1212 Safe Use of Ground Equipment training module, recognising your awareness of risk assessment, PPE and safe practice with ground equipment, fuel and chemicals.
Your Certificate of Completion
Official certification confirming you have successfully completed the WFA1212 Safe Use of Ground Equipment course and met all required training standards.
WFA Ground Safety Awareness Recognition
Confirms your awareness of safe practice with ground equipment, a recommended step before any supervised machinery training at Winnston Park.
Notes: OVERVIEW — say: WFA1212 – Safe Use of Ground Equipment sets out how the WFA expects ground equipment to be used safely. You will learn about risk assessment, training and authorisation, personal protective equipment, safe operation of mowers, rollers and powered tools, fuel and chemical safety, keeping others safe, and reporting faults and incidents. This is a WFA award, not an ECB qualification: for recognised groundsmanship training see the ECB's groundsmanship resources and courses (including its TS4 pitch and outfield guidance), and the ICC's pitch-curation guidance. The module is for every member who will work on the ground, and should be completed early in the pathway. It gives awareness of safe practice but is not a substitute for accredited machinery or chemical training, the manufacturer's instructions, or professional health and safety advice. Under-18s must not operate powered machinery and should only help with supervised, low-risk tasks. Completing it earns the WFA Ground Safety Awareness recognition.

## Slide 4
WE ARE HERE TO HELP
NEED HELP? JUST ASK
DURING THE SESSION
Put your hand up or ask your coach — there is no such thing as a silly question.
Finding it hard, or too easy? Ask — every activity can be made easier or harder.
Hurt, unwell or feeling dizzy? Stop, sit out and tell a coach straight away.
Need water, a break or the toilet? Just let a coach know.
WORRIED ABOUT SOMETHING?
If anything or anyone makes you feel unsafe or upset, tell your coach or the Welfare Officer — the same day.
You can also report a concern online at winnfamilyleague.com/association/safeguarding.
In an emergency, call 999.
AFTER THE SESSION
Questions about today? Email info@winnfamilyleague.com.
Your certificates, progress and feedback form are in the members' area — winnfamilyleague.com/my.
Free one-to-one coaching for league members, any day 9am–6pm.
Notes: NEED HELP? — read this slide out and point to where the coaches and the Welfare Officer are. Say: "If you get stuck, feel unwell or something is worrying you, tell one of us straight away. Nobody will ever be in trouble for asking for help." Check for anyone who needs an adaptation (injury, medical condition, access needs) and agree it quietly now. Stuck on a lesson or the test? Members can ask through the module page, or email the Training Centre team.

## Slide 5
YOUR LEARNING PATHWAY
WHERE THIS MODULE FITS
REQUIRED FIRST
WFA1201 Introduction to Cricket Groundsmanship
RECOMMENDED PREPARATION
No extra preparation needed.
THIS MODULE UNLOCKS
The next stage of your pathway.
Notes: REQUIRED — the test unlocks only once these are passed: WFA1201 Introduction to Cricket Groundsmanship.

## Slide 6
08
THE LESSONS
1. Why Equipment Safety Matters · 2. Risk Assessment · 3. Training and Authorisation · 4. Personal Protective Equipment · 5. Safe Operation · 6. Fuel, Batteries and Chemicals · 7. Lone Working and Emergencies · 8. Reporting Faults and Near Misses
Notes: This module has 8 lessons.

## Slide 7
LESSON 1 OF 8
WHY EQUIPMENT SAFETY MATTERS
KEY POINTS
Machines can cause serious injury instantly
Fuel and chemicals carry hazards
Most accidents have familiar causes
Good habits prevent most accidents
IN THIS LESSON
In this lesson you will learn why safety comes first on the ground. Mowers, rollers, scarifiers, strimmers and tractors can cause amputations, crushing injuries, burns and eye injuries in a moment. Fuel is flammable and turf chemicals can harm health and the environment. Most accidents come from familiar causes: untrained operators, missing guards, clearing blockages with the engine running, rushing, and people too close to working machines. Good habits prevent almost all of them. This module explains those habits, but it cannot replace accredited training, the manufacturer's instructions or professional advice.
Notes: LESSON 1 — WHY EQUIPMENT SAFETY MATTERS — say: In this lesson you will learn why safety comes first on the ground. Mowers, rollers, scarifiers, strimmers and tractors can cause amputations, crushing injuries, burns and eye injuries in a moment. Fuel is flammable and turf chemicals can harm health and the environment. Most accidents come from familiar causes: untrained operators, missing guards, clearing blockages with the engine running, rushing, and people too close to working machines. Good habits prevent almost all of them. This module explains those habits, but it cannot replace accredited training, the manufacturer's instructions or professional advice. Key points: Machines can cause serious injury instantly; Fuel and chemicals carry hazards; Most accidents have familiar causes; Good habits prevent most accidents.

## Slide 8
LESSON 2 OF 8
RISK ASSESSMENT
KEY POINTS
Identify hazards and who could be harmed
Put controls in place before starting
Read the club's written risk assessments
If it cannot be controlled, do not do it
IN THIS LESSON
In this lesson you will learn how risk assessment works. Before a task, think about what could cause harm, who might be harmed and how, and what controls are needed, such as training, guards, protective equipment, barriers or timing work when the ground is empty. The club should keep written risk assessments for its main tasks and machines, in line with health and safety law and regulations on work equipment. Read them before you start, and if anything has changed, such as weather, slope or the presence of children, stop and think again. If the risk cannot be controlled, do not do the job.
Notes: LESSON 2 — RISK ASSESSMENT — say: In this lesson you will learn how risk assessment works. Before a task, think about what could cause harm, who might be harmed and how, and what controls are needed, such as training, guards, protective equipment, barriers or timing work when the ground is empty. The club should keep written risk assessments for its main tasks and machines, in line with health and safety law and regulations on work equipment. Read them before you start, and if anything has changed, such as weather, slope or the presence of children, stop and think again. If the risk cannot be controlled, do not do the job. Key points: Identify hazards and who could be harmed; Put controls in place before starting; Read the club's written risk assessments; If it cannot be controlled, do not do it.

## Slide 9
LESSON 3 OF 8
TRAINING AND AUTHORISATION
KEY POINTS
Trained, assessed and authorised per machine
Authorisation is recorded
Under-18s must not operate powered machines
WFA badges do not authorise machine use
IN THIS LESSON
In this lesson you will learn the WFA rule on authorisation. No member may operate any powered ground machinery until they have been trained on that specific machine, assessed as competent and authorised by the club. Authorisation is recorded, and covers only the machines you have been signed off on. Read the operator's manual. Under-18s must not operate powered machinery and should only help with supervised, low-risk tasks. Recognised training is available through turf and machinery training providers, the ECB's groundsmanship programme and, for chemicals, accredited certificate of competence courses. Your WFA badge does not on its own authorise machine use.
Notes: LESSON 3 — TRAINING AND AUTHORISATION — say: In this lesson you will learn the WFA rule on authorisation. No member may operate any powered ground machinery until they have been trained on that specific machine, assessed as competent and authorised by the club. Authorisation is recorded, and covers only the machines you have been signed off on. Read the operator's manual. Under-18s must not operate powered machinery and should only help with supervised, low-risk tasks. Recognised training is available through turf and machinery training providers, the ECB's groundsmanship programme and, for chemicals, accredited certificate of competence courses. Your WFA badge does not on its own authorise machine use. Key points: Trained, assessed and authorised per machine; Authorisation is recorded; Under-18s must not operate powered machines; WFA badges do not authorise machine use.

## Slide 10
LESSON 4 OF 8
PERSONAL PROTECTIVE EQUIPMENT
KEY POINTS
Sturdy, protective footwear
Hearing and eye protection as needed
Gloves and label-specified chemical PPE
No loose clothing or jewellery
IN THIS LESSON
In this lesson you will learn about personal protective equipment, often called PPE. The right PPE depends on the task and is set out in the risk assessment. Sturdy footwear, ideally with protective toe caps, is essential around mowers and rollers. Hearing protection is needed with noisy machines. Eye protection and a face visor are important with strimmers. Gloves protect hands when handling blades, fuel or chemicals, and chemical labels may specify particular gloves, overalls or face protection. Avoid loose clothing, jewellery and long hair that could catch. PPE is the last line of defence, so it supports, not replaces, safe working.
Notes: LESSON 4 — PERSONAL PROTECTIVE EQUIPMENT — say: In this lesson you will learn about personal protective equipment, often called PPE. The right PPE depends on the task and is set out in the risk assessment. Sturdy footwear, ideally with protective toe caps, is essential around mowers and rollers. Hearing protection is needed with noisy machines. Eye protection and a face visor are important with strimmers. Gloves protect hands when handling blades, fuel or chemicals, and chemical labels may specify particular gloves, overalls or face protection. Avoid loose clothing, jewellery and long hair that could catch. PPE is the last line of defence, so it supports, not replaces, safe working. Key points: Sturdy, protective footwear; Hearing and eye protection as needed; Gloves and label-specified chemical PPE; No loose clothing or jewellery.

## Slide 11
LESSON 5 OF 8
SAFE OPERATION
KEY POINTS
Pre-use checks; never use without guards
Clear the area and keep people away
Isolate before clearing blockages
No passengers; never work impaired
IN THIS LESSON
In this lesson you will learn the core rules of safe operation. Do your pre-use checks, and never use a machine with missing or damaged guards. Clear the area of stones, balls and debris. Keep people, especially children, well away, and stop if anyone approaches. Never clear blockages or adjust blades with the engine running: stop, remove the key or spark plug lead, and wait for moving parts to stop. Take care on slopes, banks and wet grass, following the manufacturer's limits. Never carry passengers. Do not work when tired, unwell or under the influence of alcohol or drugs.
Notes: LESSON 5 — SAFE OPERATION — say: In this lesson you will learn the core rules of safe operation. Do your pre-use checks, and never use a machine with missing or damaged guards. Clear the area of stones, balls and debris. Keep people, especially children, well away, and stop if anyone approaches. Never clear blockages or adjust blades with the engine running: stop, remove the key or spark plug lead, and wait for moving parts to stop. Take care on slopes, banks and wet grass, following the manufacturer's limits. Never carry passengers. Do not work when tired, unwell or under the influence of alcohol or drugs. Key points: Pre-use checks; never use without guards; Clear the area and keep people away; Isolate before clearing blockages; No passengers; never work impaired.

## Slide 12
LESSON 6 OF 8
FUEL, BATTERIES AND CHEMICALS
KEY POINTS
Approved, labelled fuel containers
Refuel outdoors with the engine off and cool
Chemicals only by certificated people
Locked store and safety data sheets
IN THIS LESSON
In this lesson you will learn to handle fuel and chemicals safely. Store fuel in approved, labelled containers in a secure, ventilated place away from ignition sources. Refuel outdoors with the engine off and cool, never while smoking, and clean up spills. Charge batteries as the manufacturer directs. Turf chemicals such as pesticides must only be handled by people holding the appropriate certificate of competence, used exactly as the label directs, and stored in a locked, dedicated store. Follow the club's arrangements for hazardous substances, and know where the safety data sheets are kept.
Notes: LESSON 6 — FUEL, BATTERIES AND CHEMICALS — say: In this lesson you will learn to handle fuel and chemicals safely. Store fuel in approved, labelled containers in a secure, ventilated place away from ignition sources. Refuel outdoors with the engine off and cool, never while smoking, and clean up spills. Charge batteries as the manufacturer directs. Turf chemicals such as pesticides must only be handled by people holding the appropriate certificate of competence, used exactly as the label directs, and stored in a locked, dedicated store. Follow the club's arrangements for hazardous substances, and know where the safety data sheets are kept. Key points: Approved, labelled fuel containers; Refuel outdoors with the engine off and cool; Chemicals only by certificated people; Locked store and safety data sheets.

## Slide 13
LESSON 7 OF 8
LONE WORKING AND EMERGENCIES
KEY POINTS
Avoid machinery when alone
Tell someone and carry a phone
Know the first aid kit and first aiders
Call 999 or 112 for serious injuries
IN THIS LESSON
In this lesson you will learn what to do when working alone and if something goes wrong. Avoid using machinery when nobody else is at the ground, and if you must work alone, tell someone where you are and when you expect to finish, and carry a charged phone. Know where the first aid kit is and who the first aiders are. In an emergency, make the area safe if you can do so without danger, call 999 or 112 for serious injuries, and give first aid only within your training. Afterwards, report the incident to the club so lessons can be learned.
Notes: LESSON 7 — LONE WORKING AND EMERGENCIES — say: In this lesson you will learn what to do when working alone and if something goes wrong. Avoid using machinery when nobody else is at the ground, and if you must work alone, tell someone where you are and when you expect to finish, and carry a charged phone. Know where the first aid kit is and who the first aiders are. In an emergency, make the area safe if you can do so without danger, call 999 or 112 for serious injuries, and give first aid only within your training. Afterwards, report the incident to the club so lessons can be learned. Key points: Avoid machinery when alone; Tell someone and carry a phone; Know the first aid kit and first aiders; Call 999 or 112 for serious injuries.

## Slide 14
LESSON 8 OF 8
REPORTING FAULTS AND NEAR MISSES
KEY POINTS
Stop, label and report faulty equipment
Report near misses too
Keep servicing records
Store securely with keys removed
IN THIS LESSON
In this lesson you will learn why reporting matters. If a machine is damaged, a guard is loose or something does not feel right, stop using it, label it clearly as out of use and tell the lead groundsperson. Report near misses too, such as a stone thrown by a mower or a slip on a slope, because they warn of future accidents. Keep machinery serviced as the manufacturer recommends and record servicing. Store machines securely, with keys removed, so children or untrained people cannot use them. A culture of honest reporting keeps everyone at Winnston Park safe.
Notes: LESSON 8 — REPORTING FAULTS AND NEAR MISSES — say: In this lesson you will learn why reporting matters. If a machine is damaged, a guard is loose or something does not feel right, stop using it, label it clearly as out of use and tell the lead groundsperson. Report near misses too, such as a stone thrown by a mower or a slip on a slope, because they warn of future accidents. Keep machinery serviced as the manufacturer recommends and record servicing. Store machines securely, with keys removed, so children or untrained people cannot use them. A culture of honest reporting keeps everyone at Winnston Park safe. Key points: Stop, label and report faulty equipment; Report near misses too; Keep servicing records; Store securely with keys removed.

## Slide 15
FURTHER LEARNING
REFERENCE VIDEOS
GRASSCUTTING TRAINING - SAFE USE OF RIDE-ON MOWERS
chilternconsulting — Excerpts from operator training for ride-on mowers, covering key safety checks. · https://www.youtube.com/watch?v=hjRM00yyGu4
Safe use of strimmers and brushcutters
International Greenkeepers - IGFH — Safe use of strimmers at a level 2 sports turf standard, including PPE. · https://www.youtube.com/watch?v=X-vU4OXd9R8
Work Equipment Safety Explained | Machinery Hazards, LOTO & PPE Training
Ibham Veza — General machinery hazards, isolation and PPE principles that apply to ground equipment. · https://www.youtube.com/watch?v=rqs2dPWT93Q
Notes: These videos are on the module page in the members’ area. They support the lessons; watch any that help.

## Slide 16
ASSESSMENT
READY FOR THE TEST?
HOW IT WORKS
12 questions, marked instantly
80% needed to pass
Retake as often as you need
No time limit
Certificate issued automatically on a pass
Locked until you have passed: WFA1201 Introduction to Cricket Groundsmanship
Notes: ASSESSMENT — take the test from the module page in the members’ area. 12 questions, marked instantly 80% needed to pass Retake as often as you need No time limit Certificate issued automatically on a pass Locked until you have passed: WFA1201 Introduction to Cricket Groundsmanship

## Slide 17
THANK YOU
You have reached the end of WFA1212 Safe Use of Ground Equipment.
Alex Winn
League Founder & Director · Winn Family Association
Keep learning in the WFA Training Centre
Notes: CLOSE — thank the group and point them to the test and their next module.